## Slide 1
Lipo
3000 mAh
Arduino MEGA2560
SD card
50
51
52
I2C
20
SDA
21
SCL
SPI
SPI
MISO
MOSI
11
SCLK
12
13
10
CS
+7.5V
0V
A4
A5
RTC
DS1307
SCL
SDA
Address
0x68
Address
0x60
PWM
6
5
7
8
A10
A11
A9
A12
A8
A13
Throttle
Roll
Pitch
Yaw
Aux1
Aux2
RC
ESC
Rear Left
ESC
Rear Right
ESC
Front Right
ESC
Front Left
Motor
Front Left
Motor
Front Right
Motor
Rear Right
Motor
Rear Left
IMU
CMPS12
+11.1v
0v
Li Ion
2600 mAh
0V
+5V

## Slide 2: Devices (1/2)
Device | Purpose | Interface
RC-THROTTLE | RC Command | PPM- Interrupt PCINT16/PK0 pin A8
RC-ROLL | RC Command | PPM- Interrupt PCINT17/PK1 pin A9
RC-PITCH | RC Command | PPM- Interrupt PCINT18/PK2 pin A10
RC-YAW | RC Command | PPM- Interrupt PCINT19/PK3 pin A11
RC-AUX1 | RC Command | PPM- Interrupt PCINT20/PK4 pin A12
RC-AUX2 | RC Command | PPM- Interrupt PCINT21/PK5 pin A13
Motor Front Left | ESC Motor | PWM using servo lib pin 5 - Timer5
Motor Front Right | ESC Motor | PWM using servo lib pin 6 - Timer5
Motor Rear Right | ESC Motor | PWM using servo lib pin 7 - Timer5
Motor Rear Left | ESC Motor | PWM using servo lib pin 8 - Timer5

## Slide 3: Devices (2/2)
Device | Purpose | Interface | 
IMU CMPS12 | Control | I2C 0x60 | 
SD Card | Logging | SPI | 
RTC DS1307 | Logging | I2C 0x68 | 
MEGA2560 built in Led | Monitor | Digital pin 13 | 

## Slide 4: Motors
# | Position | Pin | Pin #
0 | Front Left | Motor1Pin | 5
1 | Front Right | Motor2Pin | 6
2 | Rear Right | Motor3Pin | 7
3 | Rear Left | Motor4Pin | 8

## Slide 5: ESC PWM using Servo lib MINPWM = ? MAXPWM = ?

## Slide 6: Motors rotation (1/2)
0
1
3
2
Front Left
CW
Propeller Reverse black
Rear Left
CCW
Propeller green
Front Right
CCW
Propeller green
Rear Right
CW
Propeller Reverse black
Roll
Pitch
Yaw

## Slide 7: Motors Rotation (2/2)
Roll: left/right side tilt.
  + tilted side right, speed 2 Right, slow 2 Left
  - left, speed 2 Left, slow 2 Right
Pitch: up/down tilt.
  + tilted skyward, speed 2 Front, slow 2 Rear
  - ground, speed 2 Rear, slow 2 Front
Yaw: rotation.
  + Clockwise, speed Front Left & Rear Right, slow Front Right & Rear Left
  - Counter clockwise, speed Front Right & Rear Left, slow Front Left & Rear Right
Mix result.
  ESC_command = PID = measure - command
  #define PIDMIX(X,Y,Z) ESC_command[ROLL]*X + ESC_command[PITCH]*Y + ESC_command[YAW]*Z
  motor[0] = PIDMIX(-1,-1,-1); //Front Left Increase speed if ROLL PID < 0 (drone too much tilted right, measure <0) or Increase speed if PITCH PID < 0 (drone too much tilted ground, measure <0) or Increase speed if YAW PID < 0 (drone too much Counter clockwise, measure <0)
  motor[1] = PIDMIX(+1,-1,+1); //Front Right Increase speed if ROLL PID > 0 (drone too much tilted left, measure >0) or Increase speed if PITCH PID < 0 (drone too much tilted ground, measure <0) or Increase speed if YAW PID > 0 (drone too much clockwise, measure >0)
  motor[2] = PIDMIX(+1,+1,-1); //Rear Right Increase speed if ROLL PID > 0 (drone too much tilted left, measure >0) or Increase speed if PITCH PID > 0 (drone too much tilted skyward, measure >0) or Increase speed if YAW PID < 0 (drone too much Counter clockwise, measure <0)
  motor[3] = PIDMIX(-1,+1,+1); //Rear Left Increase speed if ROLL PID < 0 (drone too much tilted right, measure <0) or Increase speed if PITCH PID > 0 (drone too much tilted skyward, measure >0) or Increase speed if YAW PID > 0 (drone too much clockwise, measure >0)

## Slide 8: Drone processing (1/3)
This processing usually occurs every 20 ms (samplePeriod), any latency is logged.
RC Command
  ROLL, PITCH: range [-45;+45]
  YAW: range [-90;+90]
  THROTTLE: 0 if < 1.1*MINPPM else value included in [1.1*MINPPM;MAXPPM]
  AUX1: 0 if < 0.9*MAXPPM else 1
  AUX2: 0 if < 0,9* MAXPPMAUX2 else 1
CMPS12
  ROLL, PITCH: range [-90;+90]
  YAW: range [0;+359]
PID computed for Roll and Pitch based on RC Command vs CMPS12 measures
  error = measure - command
  PID = (KP*error) + (KI*sum_error*sampleTime) + (KD*delta_error/ sampleTime)
  With
    Kp[3] = {0.6, 0.6, 2.4};
    Ki[3] = {0.02, 0.02, 0.01}; // values for 50hz (20 ms)
    Kd[3] = {12.0, 12.0, 0.0}; // values for 50hz (20 ms)
  NB:
    The Integral sum_error is capped to _IMax = 5
    Low pass filter cut frequency at 20 Hz for the Derivative component, cuts out the high frequency noise that can drive the controller crasy
    Initial Yaw (YawInit) is subtracted from Yaw and Yaw is converted from [0;+359] to range [-180;+180]
    Considering error max = 20, Integral max = 5 and delta error max = 20 => |PID| < 26.
Call MotorESC_RunMotors
  ESC_command[THROTTLE] = RC_command Throttle
  ESC_command[ROLL] = PID Roll
  ESC_command[PITCH] = PID Pitch
  ESC_command[YAW] = PID Yaw

## Slide 9: Drone processing (2/3)
MotorESC_RunMotors
  if ESC_command[THROTTLE] = 0 => Motors = STOPPWM
  else:
  // assure consistency between the impact of the throttle and of the PID
  throttle = map(ESC_command[THROTTLE], MINPPM, MAXPPM, MINPWMTHRO, MAXPWMTHRO); // to give room for PID ajustement
  #define PIDMIX(X,Y,Z) ESC_command[ROLL]*X + ESC_command[PITCH]*Y + ESC_command[YAW]*Z
  pid = PIDMIX(-1,-1,-1); //Front Left
  _motor[0] = map(pid, -MAXABSPID, MAXABSPID, MINPWMPID, MAXPWMPID) + throttle;
  pid = PIDMIX(+1,-1,+1); //Front Right
  _motor[1] = map(pid, -MAXABSPID, MAXABSPID, MINPWMPID, MAXPWMPID) + throttle;
  pid = PIDMIX(+1,+1,-1); //Rear Right
  _motor[2] = map(pid, -MAXABSPID, MAXABSPID, MINPWMPID, MAXPWMPID) + throttle;
  pid = PIDMIX(-1,+1,+1); //Rear Left
  _motor[3] = map(pid, -MAXABSPID, MAXABSPID, MINPWMPID, MAXPWMPID) + throttle;
#define STOPPWM 1140
#define MINPWM 1148
#define MAXPWM 1832
#define MINPWMTHRO 1250
#define MAXPWMTHRO 1750
#define MAXABSPWMPID 200
#define MAXABSPID 79 // computed based on value of the coeff and max error for PID

## Slide 10: Drone processing (3/3)
MotorESC_RunMotors (continued)
  For all motors compute:
    maxMotor = max (motor[i]- MAXPWM )
    minMotor = max (MINPWM - _motor[i])
  If maxMotor >0, then Subtract maxMotor from all motors
  If minMotor >0, then Add minMotor to all motors
  If maxMotor >0 or minMotor >0 , then Cap all motors between MINPWM and MAXPWM

## Slide 11: RC
+90° Yaw
-90° Yaw
+45° Roll
+ Front Right
+ Rear Right
-45° Roll
+Front Left
+ Rear Left
+1100/0 Throttle
+1920 Throttle
-45° Pitch
+Rear Right
+ Rear Left
+45° Pitch
+ Front Left
+ Front Right
Aux1 (0/1)
Aux2 (0/1)

## Slide 12: Motors
RPM
8 000 rpm max for stable flight ( ie video)
10 000 rpm max for standard flight
12 000 rpm max for race
Using 3S Lipo of 11,1V
8000 tours / 11.1V ≈ 720KV
10000 tours /11.1V ≈ 900KV
12000 tours / 11.1V ≈ 1100KV
I have selected: 1240kv

## Slide 13: 4 Motors Turnigy Aerodrive SK3 - 2826-1240kv Brushless Outrunner Motor (Hobby King SK3-2826-1240)
Active: 22T Tension: 2 ~ 3S Lipoly RPM / V: 1240 kv Résistance interne: 0,095 Ohm Max Chargement: 16A Puissance: 150W Shaft Dia: 3.0mm Trous de boulons: 16mm et 19mm Fil de Bolt: M3 Poids: 45g Branchez Moteur: 3.5mm Bullet Connecto

## Slide 14: Propeller
Size
  A so-called long propeller will spin slower than a short propeller. Its lift capacity, however, will naturally be more important because of its size. Moreover, its size brings stability in flight. A short propeller will spin faster than a long propeller. It will have less lift but will bring reactivity in flight
Pitch
  A high pitch implies a low lift but a high maximum rotation speed. A lower step implies better lift but a limited maximum speed of rotation (by compensation).
I have selected:
  size: 10 pouces (25,4 cm) => length frame > 23 cm length min=(25.4+6.5)√2
  pitch: 4.5 pouces (10,2 cm)
ClockWise: GWS style slowfly Hélice 10x4.5 Noir (CW)(Hobby King 9329000027)
CounterClockWise: GWS style slowfly Hélice 10x4.5 Green (CCW) (Hobby King 9329000028)

## Slide 15
Electronic Speed Controller ESC
Courant max Motor: 16A
ESC 20A
I have selected Turnigy AE-20A Brushless ESC (Hobby king TAE-20A)
  Sortie: 20A continue, éclater 25A jusqu'à 10 secondes. Tension d'entrée: 2-4 cellules batterie lithium ou 5-12 cellules de batterie NIMH. BEC: Linéaire 2A @ 5V (not used) Transmission Control Signal: système opto couplé. Vitesse maximale: 2 Pole: 210,000rpm 6 Pole: 70,000rpm 12 Pole: 35,000rpm Taille: 50mm (L) * 26mm (W) * 12mm (H). Poids: 19g.
The BEC power is 5v < 7v min needed for Arduino MEGA2560, so I don’t use the BEC.

## Slide 16: Configuration ESC

## Slide 17: Lipo
3S :3*3,7v =11,1v
4 motors 16A => 64A Max
I have selected LiPo 3S 3000mAh 11.1V 30C not too much heavy with Max discharge = 3*30 = 90A > 64A
Specifications
  Type de la batterie LiPO
  Capacité batterie 3300 (mAh)
  Voltage 11.1 (V)
  Courant décharge en continu 30 (C)
  Courant de décharge max 60 (C)
  Poids 182 (g)
  Longueur 103 (mm)
  Largeur 33 (mm)
  Hauteur 23 (mm)
  Type de prise Dean / Tplug
  Prise Equilibrage JST-XH
  Taux de Charge Max 2 (C)
  Nombre d'éléments 3 (S)

## Slide 18: Charger Graupner ULTRAMAT 16
Lithium batteries: Lipo (motors) and Lilo (Arduino)
  The max. charge voltage for LiPo is 4.2V, for LiIo 4.1V, for LiFe 3.6V. To store the batteries, adjust the charge voltage about 0.4V lower as the maximum charge voltage
  At charging/discharging the battery types will be displayed as followed:
    LiPo (LiMn) = LP
    LiIo = LI
    LiFe = LF
  Lithium batteries are usually charged at the 1C rate
Ni-MH batteries (RC transmitter)

## Slide 19: Receiver
Receiver Henge RP62L
Spécifications:
Size: 49x24x14mm
Weight: 9.2g (with shrink wrap)
Sensitivity: better than 2.0μV
Selectivity: ±8kHz at 65dB down
No. of channels: 1-6
RF technology: Dual tuned RF circuitry
Analog filtering: Dual 4 pole ceramic filter
Digital filtering: DSP filtering with mild algorithm
Modulation: FM/PPM
Shift polarity: Positive or Negative (auto detect)
Case: Shrink wrap
Operating Voltage: 4.8V~6.0VDC
Operating Current: 24mA.

## Slide 20: Frame
HobbyKing X550 en fibre de verre Quadcopter Cadre 550mm (9323000036)
Spécifications:
  Poids: 312g Largeur: 550mm Trous Motor Bolt: largeur de 19mm
  But the frame has been reduced from 10cm, new Largeur: 450mm

## Slide 21: Special pins Arduino MEGA2560
Pin Change Interrupt 2 ISR(PCINT2_vect)
For pins PCINT16-PCINT23 (PK0- PK7), PORT K
Use pin A8 to A13 (PCINT16 to PCINT21 )
PCMSK2 – Pin Change Mask Register 2 Bit 2 – PCIF2: clear any outstanding interrupts 2
PCIFR – Pin Change Interrupt Flag Register => Bit 2 – PCIF2: clear any outstanding interrupts 2
PCICR – Pin Change Interrupt Control Register => Bit 2 – PCIE2: enable pin change interrupts 2
SPI
Pin #10: CS
pin #11->pin #51
pin #12->pin #50
pin #13->pin #52