## Slide 1
Arduino MEGA2560
Address
0x60
Serial 2
22
23
24
17
RX
16
TX
SD card
50
51
52
Digital
Int 1
3
Int1
A2
Brightness
TEMT6000
TWI
20
SDA
21
SCL
Temperature
TMP102
Compass
CMPS03
Address
0x48
SPI
Serial 3
15
RX
14
TX
Buzzer DFR0032
IOT WIFIServer
ESP8266
LiquidCrystal
Address
0x20
SPI
TXD
RXD
MISO
MOSI
11
SCLK
12
13
8
CS
0V
+5V
+5V
0V
+3V
0V
Camera
LSY201
25
+5V
0V
A1
IR
GP2Y0A21YK
Contact Left
26
Contact Right
27
+5V
PWM
Tilt&Pan Horiz
44
Tilt&Pan Vert.
45
Servo IR
46
MotionSEN0018
28
Serial 1
19
RX
18
TX
IOT WIFClient
ESP8266

## Slide 2
HBridge
HBridge
Arduino MEGA2560
D
IGITAL
PWM
5
4
Motor right #1 In
30
+0v
31
33
32
6
7
Motor right #1 Enable
Motor right #2 Enable
Motor right #2 In
Motor right #2
(rear)
Motor right #1
(front)
Motor left #1 In
Motor left #1 Enable
Motor left #2 Enable
Motor left #2 In
Motor left #2
(rear)
Motor left #1 (front)
+7.4v
+0v
Lipo
+
+
+
+
-
-
-
-

## Slide 3: Devices (1/2)
Device | Purpose |  | 
Motor right #1 Right front | Run | PWM Enable pin 4 In Digital pin 30 | 
Motor right #2 Right rear | Run | PWM Enable pin 5 In Digital pin 31 | 
Motor left #1 Left front | Run | PWM Enable pin 7 In Digital pin 33 | 
Motor left #2 Left rear | Run | PWM Enable pin 6 In Digital pin 32 | 
IR | Run | Analogic pin A1 | 
Servo for IR | Run | PWM pin 46 | 
Contact left | Run | Digital pin 26 | 
Contact right | Run | Digital pin 27 | 
Compas | Run | I2C | 

## Slide 4: Devices (2/2)
Device | Purpose | Connection | 
LCD | Monitor | I2C | 
Led green | Monitor | Digital pin 22 | 
Led red | Monitor | Digital pin 23 | 
Led bleue | Monitor | Digital pin 24 | 
Buzzer | Monitor | Digital pin 25 | 
Camera | Alert | I2C | 
Tilt&Pan servos for Camera | Alert | PWM pin 44&45 | 
Sd Card | Alert | SPI | 
Brightness sensor | Detect | Analogic pin A2 | 
Temperature sensor | Detect | I2C | 
Motion sensor | Detect | Digital pin 28 | 

## Slide 5
Arduino
ESP8266
IoTWiFiServer
SSID:
WIFICOTEAU2
Int
Serial
38400 bauds
192.168.0.9:80
/robotCmd
IOTSsend
IOTSread
4
8
RXI
7
TX0
ESP8266
IoTWiFiClient
Serial1
38400 bauds
IOTSread
8
RXI
7
TXO
PI
/var/www/html/
robotInfos.php,
robotInfos.txt,
robotInfos.log
/var/www/html/
robotPicture.php,
robotPicture.log
/var/log/apache2/
error.log
192.168.0.18:8080
/robotInfos.php or
/robotPicture.php
IOTSread
IOTSsend
IOTSsend
3
int1
17
RX
16
TX
18
TX
19
RX
IOTSread
IOTSsend
Serial2
38400 bauds
Serial
38400 bauds
INFOS: Content-Type: application/x-www-form-urlencoded
PICTURE: Content-Type: multipart/form-data; boundary=AaB03x
Content-Disposition: form-data
Content-Type: image/jpeg
Content-Transfer-Encoding: binary
HTTP
5
5
MySQL
ROBOT
edh@edh
Mail infos +
Mail pictures

## Slide 6: Serial IOT message
SBN1 (0xFA)
SBN2 (0xFB)
TAGSYMBOL (0x23 - ‘#’)
TAG_CMDID (0x49 - ‘I’)
0
cmdId : id of the commande (1,2,3….)
TAGSYMBOL (0x23 - ‘#’)
For each parameter i:
  TAGSYMBOL (0x23 - ‘#’)
  TAGSYMBOL (0x50 - ‘P’)
  Parameter i (high byte)
  Parameter i (low byte)
EBN1 (0xFE)
EBN2 (0xFF)
RESP_OK or RESP_KO | CMD | INFOS | PICTURE
TAG_RESP (0x52 - ‘R’) | TAG_CMD (0x43 - ‘C’) | TAG_INFOS (0x46 - ‘F’) | TAG_PICTURE (0x55 - ‘U’)
0 | 0 | 0 | 0
RESP_OK 2 RESP_KO 3 | CMD_START 0x01 CMD_STOP 0x02 CMD_INFOS 0x03 CMD_PICTURE 0x04 CMD_TURN 0x05 CMD_CHECK_AROUND 0x06 CMD_MOVE_TILT_PAN 0x07 CMD_GO 0x08 CMD_ALERT 0x09 CMD_CHECK 0x0A CMD_PI 0x0B | paramlen | paramlen

## Slide 7: Serial IOT messages
Server send CMD to the Robot
IOTSsend(0, CMD, CMD_INFOS, param, 0, _cmdId); // send the command INFOS to the Robot
IOTSsend(0, CMD, cmd, param, paramlen, _cmdId); // send the command to the Robot
Robot send RESP to the Server followin reception CMD
IOTSsend(2, RESP_KO);
IOTSsend(2, RESP_OK, resp, resplen, cmdId);
Robot send INFOS and PICTURE to the Client
IOTSsend (1, INFOS, resp, resplen);
IOTSsend(1, PICTURE, param, paramlen);
Client send RESP to the Robot following reception PICTURE
IOTSsend(0, RESP_OK);

## Slide 8: Interuptions Arduino MEG2560
Pin #2 = interruption #0 Pin #3 = interruption #1 Pin #18 = interruption #5 Pin #19 = interruption #4 Pin #20 = interruption #3 Pin #21 = interruption #2