## Slide 1
Lipo
3000 mAh
Arduino MEGA2560
50
51
52
+7.5V
0V
Digital
24
25
23
22
A10
A11
A9
A12
A8
A13
Throttle
Roll
Pitch
Yaw
Aux1
Aux2
RC
ESC
Front
Right
ESC
Rear Right
ESC
Rear Left
ESC
Front Left
Motor
Front Left (3)
Motor
Rear Left (2)
Motor
Rear Right (1)
Motor
Front Right (0)
GND IMU
VIN ICM20948
MOSI
SCLK
MISO
CS
+11.1v
0v
Li Ion
2600 mAh
GND
+5V
+3,3V
53
CS
SCLK
MOSI
MISO
SPI
SD card
SPI
MISO
MOSI
11
SCLK
12
13
10
CS
9
8
Led
Init
Led
Running

## Slide 2: Devices (1/2)
Device | Purpose | Interface
RC-THROTTLE | RC Command | PPM- Interrupt PCINT16/PK0: pin A8
RC-ROLL | RC Command | PPM- Interrupt PCINT17/PK1: pin A9
RC-PITCH | RC Command | PPM- Interrupt PCINT18/PK2: pin A10
RC-YAW | RC Command | PPM- Interrupt PCINT19/PK3: pin A11
RC-AUX1 | RC Command | PPM- Interrupt PCINT20/PK4: pin A12
RC-AUX2 | RC Command | PPM- Interrupt PCINT21/PK5: pin A13
ESC 0 | Motor Front Right | PORTA bit0 pin 22
ESC 1 | Motor Rear Right | PORTA bit1 pin 23
ESC 2 | Motor Rear Left | PORTA bit2 pin 24
ESC 3 | Motor Front Left | PORTA bit3 pin 25

## Slide 3: Devices (2/2)
Device | Purpose | Interface
IMU ICM20948 | Control | SPI MISO: pin D50 MOSI: pin D51 SCLK: pin D52 CS: pin D53
SD Card | Logging | SPI MISO: pin D12-D50 MOSI: pin D51-D11 SCLK: pin D13-D52 CS: pin D10
Led Init Led Running | Monitor | pin D8 pin D9

## Slide 4: System
Function | Purpose | System component | 
micros() | time | Timer0 | 
ISR (PCINT2_vect) // ISR(PCINT2_vect){} for pins PCINT16-PCINT23 (PK0- PK7) | RC | Interrupt Pin change | 

## Slide 5: Special pins Arduino MEGA2560
Pin Change Interrupt 2 ISR(PCINT2_vect)
For pins PCINT16-PCINT23 (PK0- PK7), PORT K
Use pin A8 to A13 (PCINT16 to PCINT21 )
PCMSK2 – Pin Change Mask Register 2 Bit 2 – PCIF2: clear any outstanding interrupts 2
PCIFR – Pin Change Interrupt Flag Register => Bit 2 – PCIF2: clear any outstanding interrupts 2
PCICR – Pin Change Interrupt Control Register => Bit 2 – PCIE2: enable pin change interrupts 2
SPI
Pin #10 (SD Card) and #53 (MPU): CS
pin #11->pin #51
pin #12->pin #50
pin #13->pin #52

## Slide 6: Startup
Blink led init 30s => Move the drone in all axes to calibrate MEMS in MPU
Turn off led init
Blink led init 15s => Connect power to ESC
Turn on led init => End init
Turn on led Running => Drone tunning
Turn of led Running => Drone stopped

## Slide 7: Motors rotation
3
0
2
1
Front Left
CW
Propeller Reverse black
Rear Left
CCW
Propeller green
Front Right
CCW
Propeller green
Rear Right
CW
Propeller Reverse black
Roll
Pitch
Yaw

## Slide 8: RC
+90 ° Yaw
-90° Yaw
+45° Roll
-45° Roll
+1100 or 0 Throttle
+1920 Throttle
-45° Pitch
+45° Pitch
Aux1 (0/1)
Aux2 (0/1)

## Slide 9: Motors
RPM
8 000 rpm max for stable flight ( ie video)
10 000 rpm max for standard flight
12 000 rpm max for race
Using 3S Lipo of 11,1V
8000 tours / 11.1V ≈ 720KV
10000 tours /11.1V ≈ 900KV
12000 tours / 11.1V ≈ 1100KV
I have selected: 920kv

## Slide 10: 4 Motors Turnigy Aerodrive SK3 2830-920kv Brushless Outrunner Motor (Hobby King 9192000242-0)
Voltage: 6.4~12.6V (2~3S LiPoly) RPM/V: 920kv Max Power: 165W Max current: 17A = > Suggested ESC: 20A Idle current: 0.95A Resistance: 140mh Shaft: 3mm Bolt holes spacing: 16 x 19mm Bolt thread: M2 Plug: 3.5mm Bullet Motor dimensions: 30 x 28mm Weight: 55g

## Slide 11: Propeller
Size
  A so-called long propeller will spin slower than a short propeller. Its lift capacity, however, will naturally be more important because of its size. Moreover, its size brings stability in flight. A short propeller will spin faster than a long propeller. It will have less lift but will bring reactivity in flight
Pitch
  A high pitch implies a low lift but a high maximum rotation speed. A lower pitch implies better lift but a limited maximum speed of rotation (by compensation).
I have selected:
  size: 10 pouces (25,4 cm) => length frame > 23 cm length min=(25.4+6.5)√2
  pitch: 4.5 pouces (10,2 cm)
ClockWise: GWS style slowfly Hélice 10x4.5 Noir (CW)(Hobby King 9329000027)
CounterClockWise: GWS style slowfly Hélice 10x4.5 Green (CCW) (Hobby King 9329000028)

## Slide 12
Electronic Speed Controller ESC
Courant max Motor: 17A
ESC > 20A
I have selected XTVTX 35A BLHeli-S
  Constant Current: 35A Peak Current: 45A Input Voltage: 2 - 6S BEC: None Dimensions: 28.5 x 13mm Weight: 6g

## Slide 13
Configuration ESC
Run BLHeliSuite
Select SILABS BLHeli Bootloader (USB/Com) in tab ATMEL/SILABS Interface
Connect ESC pin 51
Select port and baud 19200
Click on Connect
Click on Read Setup
Make changes PPM Min = 1000
Make changes PPM Max = 2000
Set Motor Direction = Reversed
for motors CCW
Click on Write Setup
Click on Flash BLHELI
Configuration

## Slide 14: Lipo
3S :3*3,7v =11,1v
4 motors 17A => 68A Max
I have selected LiPo 3S 3000mAh 11.1V 30C not too much heavy with Max discharge = 2*30 = 60A ~ 68A
Specifications
  Type de la batterie LiPO
  Capacité batterie 3300 (mAh)
  Voltage 11.1 (V)
  Courant décharge en continu 30 (C)
  Courant de décharge max 60 (C)
  Poids 182 (g)
  Longueur 103 (mm)
  Largeur 33 (mm)
  Hauteur 23 (mm)
  Type de prise Dean / Tplug
  Prise Equilibrage JST-XH
  Taux de Charge Max 2 (C)
  Nombre d'éléments 3 (S)

## Slide 15: Charger Graupner ULTRAMAT 16
Lithium batteries: Lipo (motors) and Lilo (Arduino)
  The max. charge voltage for LiPo is 4.2V, for LiIo 4.1V, for LiFe 3.6V. To store the batteries, adjust the charge voltage about 0.4V lower as the maximum charge voltage
  At charging/discharging the battery types will be displayed as followed:
    LiPo (LiMn) = LP
    LiIo = LI
    LiFe = LF
  Lithium batteries are usually charged at the 1C rate
Ni-MH batteries (RC transmitter)

## Slide 16: Receiver
Receiver Henge RP62L
Spécifications:
Size: 49x24x14mm
Weight: 9.2g (with shrink wrap)
Sensitivity: better than 2.0μV
Selectivity: ±8kHz at 65dB down
No. of channels: 1-6
RF technology: Dual tuned RF circuitry
Analog filtering: Dual 4 pole ceramic filter
Digital filtering: DSP filtering with mild algorithm
Modulation: FM/PPM
Shift polarity: Positive or Negative (auto detect)
Case: Shrink wrap
Operating Voltage: 4.8V~6.0VDC
Operating Current: 24mA.

## Slide 17: Frame
HobbyKing X550 en fibre de verre Quadcopter Cadre 550mm (9323000036)
Spécifications:
  Poids: 312g Largeur: 550mm Trous Motor Bolt: largeur de 19mm
  But the frame has been reduced from 10cm, new Largeur: 450mm