## Slide 1
SSID:
WIFICOTEAU
SSID:
WIFICOTEAU2
SSID:
WIFICOTEAU2
Arduino
ESP8266
IoTWiFiServer
MAC: F7:C9:5B:7F:CF:5C
IP Fixe: 192.168.0.30
SSID:
WIFICOTEAU
Int
Serial
38400 bauds
192.168.0.30:80
/robotCmd
IOTSsend
IOTSread
4
8
RXI
7
TX0
ESP8266
IoTWiFiClient
MAC: 18:FE:34:F1:75:BE
IP Fixe: 192.168.0.31
Serial1
38400 bauds
IOTSread
8
RXI
7
TXO
PI
MAC: 00:0f:13:37:1b:c8
IP Fixe: 192.168.0.18
/var/www/html/
robotInfos.php,
robotInfos.txt,
robotInfos.log
/var/www/html/
robotPicture.php,
robotPicture.log
/var/log/apache2/
error.log
192.168.0.18:8080
/robotInfos.php or
/robotPicture.php
IOTSread
IOTSsend
IOTSsend
3
int1
17
RX
16
TX
18
TX
19
RX
IOTSread
IOTSsend
Serial2
38400 bauds
Serial
38400 bauds
INFOS: Content-Type: application/x-www-form-urlencoded
PICTURE: Content-Type: multipart/form-data; boundary=AaB03x
Content-Disposition: form-data
Content-Type: image/jpeg
Content-Transfer-Encoding: binary
HTTP
5
5
MySQL
ROBOT
edh@edh
Mail infos +
Mail pictures
Ground
Ground
Ground
Ground

## Slide 2
Arduino MEGA2560
Serial 1
22
23
24
19
RX
18
TX
SD card
50
51
52
Digi
tal
Int 1
3
Int1
TWI
20
SDA
21
SCL
ToF
VL530LX
Compass
CMPS12
Address
0x29
SPI
Serial 3
15
RX
14
TX
Buzzer DFR0032
IOT WIFIServer
ESP8266
LCD
LiquidCrystal
Address
0x20
SPI
TXD
RXD
MISO
MOSI
11
SCLK
12
13
10
CS
0V
+5V
0V
Camera
LSY201
25
+5V
0V
A0
IR Sharp
GP2Y0A21Y
Contact Left
26
Contact Right
27
+5V
PWM
Tilt&Pan Horiz
44
Tilt&Pan Vert.
45
Servo IR
46
MotionSEN0018
28
Serial 2
17
RX
16
TX
IOT WIFIServer
ESP8266
0V
°C & %H DHT22
34
220 Ω
220 Ω
220 Ω
A4
A5
RTC
DS1307
SCL
SDA
Address
0x68
Address
0x60
Brightness
BH1720
Address
0x23

## Slide 3
HBridge
HBridge
Arduino MEGA2560
D
IGITAL
PWM
5
4
Motor right #1 In
30
+0v
31
33
32
6
7
Motor right #1 Enable
Motor right #2 Enable
Motor right #2 In
Motor right #2
(rear)
Motor right #1
(front)
Motor left #1 In
Motor left #1 Enable
Motor left #2 Enable
Motor left #2 In
Motor left #2
(rear)
Motor left #1 (front)
+7.4v
+0v
Lipo
+
+
+
+
-
-
-
-

## Slide 4: Devices (1/2)
Device | Purpose |  | 
Motor right #1 Right front | Run | PWM Enable pin 4 In Digital pin 30 | 
Motor right #2 Right rear | Run | PWM Enable pin 5 In Digital pin 31 | 
Motor left #1 Left front | Run | PWM Enable pin 7 In Digital pin 33 | 
Motor left #2 Left rear | Run | PWM Enable pin 6 In Digital pin 32 | 
Contact left | Run | Digital pin 26 | 
Contact right | Run | Digital pin 27 | 
Sharp IR | Run | Analogic pin A0 | 
Servo for IR | Run | PWM pin 46 | 
ToF | Run | I2C 0x29 | 
Compass | Run | I2C 0x60 | 

## Slide 5: Devices (2/2)
Device | Purpose | Connection | 
LCD | Monitor | I2C 0x20 | 
Led green | Monitor | Digital pin 22 | 
Led red | Monitor | Digital pin 23 | 
Led bleue | Monitor | Digital pin 24 | 
Buzzer | Monitor | Digital pin 25 | 
Camera | Alert | Serial3 | 
Tilt&Pan servos for Camera | Alert | PWM pin 44&45 | 
Sd Card | Alert | SPI | 
RTC | Alert | I2C 0x68 | 
Brightness sensor | Detect | I2C 0x23 | 
Temperature & Humidity sensor | Detect | Digital pin 34 | 
Motion sensor | Detect | Digital pin 28 | 
Sound sensor | Detect |  | 

## Slide 6: Serial IOT message
SBN1 (0xFA)
Length = 8+(4*paramlen). NOTA: Arduino HardwareSerial.h has been changed in order to increase the buffers SERIAL_TX_BUFFER_SIZE and SERIAL_RX_BUFFER_SIZE from 64 to 128 (same as ESP8266). The serial messages greater than 128 bytes fail.
SBN2 (0xFB)
TAGSYMBOL (0x23 - ‘#’)
TAG_CMDID (0x49 - ‘I’)
0
cmdId : id of the command (1,2,3….) provided only for CMD and RESP_OK.
TAGSYMBOL (0x23 - ‘#’)
For each parameter i:
  TAGSYMBOL (0x23 - ‘#’)
  TAGPARAM (0x50 - ‘P’)
  Parameter i (high byte)
  Parameter i (low byte)
EBN1 (0xFE)
EBN2 (0xFF)
RESP_OK or RESP_KO | CMD | INFOS | PICTURE
TAG_RESP (0x52 - ‘R’) | TAG_CMD (0x43 - ‘C’) | TAG_INFOS (0x46 - ‘F’) | TAG_PICTURE (0x55 - ‘U’)
0 | 0 | 0 | 0
RESP_OK 2 RESP_KO 3 | CMD_START 0x01 CMD_STOP 0x02 CMD_GET_INFOS 0x03 CMD_PICTURE 0x04 CMD_TURN 0x05 CMD_CHECK_AROUND 0x06 CMD_MOVE_TILT_PAN 0x07 CMD_GO 0x08 CMD_ALERT 0x09 CMD_CHECK 0x0A CMD_PI 0x0B CMD_TEST 0x0C | paramlen | paramlen

## Slide 7: Serial IOT messages
Server send the command (CMD) to the Robot
IOTSsend(0, CMD, cmd, param, paramlen, _cmdId); // send the command to the Robot
Robot send (RESP) to the Server following the reception of the command (CMD)
IOTSsend(2, RESP_KO);
IOTSsend(2, RESP_OK, resp, resplen, cmdId);
Robot send INFOS and PICTURE to the Client
IOTSsend (1, INFOS, resp, resplen); the response
IOTSsend(1, PICTURE, param, paramlen);
Client send the response (RESP) to the Robot following the reception of the PICTURE
IOTSsend(0, RESP_OK);

## Slide 8: Commandes
Commande | Purpose | 
Test IOT | Test communication with the ESP8266 server | 
Check every n sec | Check every n seconds | 
Stop | Stop | 
Picture | Make picture and return the picture number | 
Move Tilt&Pan | Move Tilt&Pan Horizontaly and Verticaly | 
Check around | Check if there is an obstacle and return the result | 
Get infos | Get infos and return them | 
PI Communication mode | Define the communication mode between the Robot and the Raspberry PI: None Alert only Alert and Infos every n seconds | 

## Slide 9: Special pins Arduino MEGA2560
Interruptions
Pin #2 = interruption #0 Pin #3 = interruption #1 Pin #18 = interruption #5 Pin #19 = interruption #4 Pin #20 = interruption #3 Pin #21 = interruption #2
SPI
Pin #10: CS
pin #11->pin #51
pin #12->pin #50
pin #13->pin #52