## Slide 1
Lipo
1500 mAh
Arduino MEGA2560
SD card
50
51
52
I2C
20
SDA
21
SCL
SPI
SPI
MISO
MOSI
11
SCLK
12
13
10
CS
+7.5V
0V
A4
A5
RTC
DS1307
SCL
SDA
Address
0x68
Address
0x60
PWM
4
3
5
6
A10
A11
A9
A12
A8
A13
Throttle
Roll
Pitch
Yaw
Aux1
Aux2
RC
ESC
Front Left
ESC
Front Right
ESC
Rear Right
ESC
Rear Left
Motor
Rear Left
Motor
Rear Right
Motor
Front Right
Motor
Front Left
IMU
CMPS12
+11.1v
0v
Li Ion
2600 mAh
0V
+5V

## Slide 2: Devices (1/2)
Device | Purpose | Interface | 
RC-THROTTLE | RC Command | PPM- Interrupt PCINT16/PK0 pin A8 | 
RC-ROLL | RC Command | PPM- Interrupt PCINT17/PK1 pin A9 | 
RC-PITCH | RC Command | PPM- Interrupt PCINT18/PK2 pin A10 | 
RC-YAW | RC Command | PPM- Interrupt PCINT19/PK3 pin A11 | 
RC-AUX1 | RC Command | PPM- Interrupt PCINT20/PK4 pin A12 | 
RC-AUX2 | RC Command | PPM- Interrupt PCINT21/PK5 pin A13 | 
Motor Front Left | ESC Motor | PWM pin 3 | 
Motor Front Right | ESC Motor | PWM pin 4 | 
Motor Rear Right | ESC Motor | PWM pin 5 | 
Motor Rear Left | ESC Motor | PWM pin 6 | 

## Slide 3: Devices (2/2)
Device | Purpose | Interface | 
IMU CMPS12 | Control | I2C 0X60 | 
SD Card | Logging | SPI | 
RTC DS1307 | Logging | I2C 0x68 | 

## Slide 4: Motors
# | Position | Pin | Pin #
0 | Front Left | Motor1Pin | 3
1 | Front Right | Motor2Pin | 4
2 | Rear Right | Motor3Pin | 5
3 | Rear Left | Motor4Pin | 6

## Slide 5: Motors rotation (1/2)
0
1
3
2
Front Left
Rear Left
Front Right
Rear Right
+ Roll -
-
Pitch
+
-
Yaw
+

## Slide 6: Motors Rotation (2/2)
Roll: left/right side tilt.
  + tilted side right, speed 2 Right, slow 2 Left
  - left, speed 2 Left, slow 2 Right
Pitch: up/down tilt.
  + tilted skyward, speed 2 Front, slow 2 Rear
  - ground, speed 2 Rear, slow 2 Front
Yaw: rotation.
  + Clockwise, speed Front Left & Rear Right, slow Front Right & Rear Left
  - Counter clockwise, speed Front Right & Rear Left, slow Front Left & Rear Right

## Slide 7: Drone Command (1/3)
RC Command
  for ROLL, PITCH, YAW: range [-90;+90]
  for THROTTLE: 0 (if < 1.1*MINPPM) or value included in [1.1*MINPPM;MAXPPM]
  for AUX1: 0 (if < 0.9*MAXPPM) else 1
  for AUX2: 0 (if < 0,9* MAXPPMAUX2 ) else 1
CMPS12
  for ROLL, PITCH: range [-90;+90]
PID computed for Roll and Pitch based on RC Command vs CMPS12 measures
  error = command – measure => error > 0 means increase command.
  PID = (0.6*error) + (0.1*sum_error*sampleTime) + (0.3*delta_error/ sampleTime)
  NB:
    The Integral component is capped to 5°
    Low pass filter cut frequency at 20 Hz for the Derivative component, cuts out the high frequency noise that can drive the controller crazy
Call MotorESC_RunMotors
  ESC_command[THROTTLE] = RC_command Throttle
  ESC_command[ROLL] = PID Roll
  ESC_command[PITCH] = PID Pitch
  ESC_command[YAW] = 0

## Slide 8: Drone Command (2/3)
MotorESC_RunMotors
  if ESC_command[THROTTLE] = 0 => Motors = MINPWM
  else:
  throttle = map(ESC_command[THROTTLE], MINPPM, MAXPPM, MINPWM, MAXPWM);
  throttle = constrain(throttle, MINPWM, MAXPWMTHRO); // to give room for PID ajustement
  PIDMIX(X,Y,Z) ESC_command[ROLL]*X + ESC_command[PITCH]*Y + ESC_command[YAW]*Z + ESC_command[THROTTLE]
  motor[0] = PIDMIX(+1,-1,-1); //Front Left
  motor[1] = PIDMIX(-1,-1,+1); //Front Right
  motor[2] = PIDMIX(-1,+1,-1); //Rear Right
  motor[3] = PIDMIX(+1,+1,+1); //Rear Left
  for(i=0; i< NBMOTORS; i++) {
  _motor[i] = map(_motor[i], -90, 90, -(MAXPWM-MINPWM)/2, (MAXPWM-MINPWM)/2);
  _motor[i] = _motor[i] + throttle;
  }

## Slide 9: Drone Command (3/3)
MotorESC_RunMotors (continued)
  Compute maxMotor = max (MAXPWM - _motor[i]) and minMotor = max (MINPWM - _motor[i])
  for all motors
  Subtract maxMotor from all motors
  Add minMotor to all motors
  Cap all motors between MINPWM and MAXPWM

## Slide 10: Special pins Arduino MEGA2560
Interruptions
Pin #2 = interruption #0 Pin #3 = interruption #1 Pin #18 = interruption #5 Pin #19 = interruption #4 Pin #20 = interruption #3 Pin #21 = interruption #2
SPI
Pin #10: CS
pin #11->pin #51
pin #12->pin #50
pin #13->pin #52