## Slide 1
Lipo
1500 mAh
Arduino MEGA2560
SD card
50
51
52
I2C
20
SDA
21
SCL
SPI
SPI
MISO
MOSI
11
SCLK
12
13
10
CS
+7.5V
0V
A4
A5
RTC
DS1307
SCL
SDA
Address
0x68
Address
0x60
PWM
6
5
7
8
A10
A11
A9
A12
A8
A13
Throttle
Roll
Pitch
Yaw
Aux1
Aux2
RC
ESC
Rear Left
ESC
Rear Right
ESC
Front Right
ESC
Front Left
Motor
Front Left
Motor
Front Right
Motor
Rear Right
Motor
Rear Left
IMU
CMPS12
+11.1v
0v
Li Ion
2600 mAh
0V
+5V

## Slide 2: Devices (1/2)
Device | Purpose | Interface
RC-THROTTLE | RC Command | PPM- Interrupt PCINT16/PK0 pin A8
RC-ROLL | RC Command | PPM- Interrupt PCINT17/PK1 pin A9
RC-PITCH | RC Command | PPM- Interrupt PCINT18/PK2 pin A10
RC-YAW | RC Command | PPM- Interrupt PCINT19/PK3 pin A11
RC-AUX1 | RC Command | PPM- Interrupt PCINT20/PK4 pin A12
RC-AUX2 | RC Command | PPM- Interrupt PCINT21/PK5 pin A13
Motor Front Left | ESC Motor | PWM pin 5 Timer 3* prescaler=64 => freq PWM 490 Hz
Motor Front Right | ESC Motor | PWM pin 6 Timer 4 prescaler=64 => freq PWM 490 Hz
Motor Rear Right | ESC Motor | PWM pin 7 Timer 4 prescaler=64 => freq PWM 490 Hz
Motor Rear Left | ESC Motor | PWM pin 8 Timer 4 prescaler=64 => freq PWM 490 Hz
*Not use pin 4 as linked to Timer 0 which is already use for millis()

## Slide 3: Devices (2/2)
Device | Purpose | Interface | 
IMU CMPS12 | Control | I2C 0X60 | 
SD Card | Logging | SPI | 
RTC DS1307 | Logging | I2C 0x68 | 
MEGA2560 built in Led | Monitor | Digital pin 13 | 

## Slide 4: Motors
# | Position | Pin | Pin #
0 | Front Left | Motor1Pin | 3
1 | Front Right | Motor2Pin | 4
2 | Rear Right | Motor3Pin | 5
3 | Rear Left | Motor4Pin | 6

## Slide 5: Motors rotation (1/2)
0
1
3
2
Front Left
CW
Propeller Reverse black
Rear Left
CCW
Propeller green
Front Right
CCW
Propeller green
Rear Right
CW
Propeller Reverse black
+ Roll -
-
Pitch
+
-
Yaw
+

## Slide 6: Motors Rotation (2/2)
Roll: left/right side tilt.
  + tilted side right, speed 2 Right, slow 2 Left
  - left, speed 2 Left, slow 2 Right
Pitch: up/down tilt.
  + tilted skyward, speed 2 Front, slow 2 Rear
  - ground, speed 2 Rear, slow 2 Front
Yaw: rotation.
  + Clockwise, speed Front Left & Rear Right, slow Front Right & Rear Left
  - Counter clockwise, speed Front Right & Rear Left, slow Front Left & Rear Right
Mix result.
  #define PIDMIX(X,Y,Z) ESC_command[ROLL]*X + ESC_command[PITCH]*Y + ESC_command[YAW
  motor[0] = PIDMIX(-1,+1,+1); //Front Left
  motor[1] = PIDMIX(+1,+1,-1); //Front Right
  motor[2] = PIDMIX(+1,-1,+1); //Rear Right
  motor[3] = PIDMIX(-1,-1,-1); //Rear Left

## Slide 7: Drone processing (1/3)
This processing usually occurs every 20 ms (samplePeriod), any latency is logged.
RC Command
  ROLL, PITCH: range [-45;+45]
  YAW: range [-90;+90]
  THROTTLE: 0 if < 1.1*MINPPM else value included in [1.1*MINPPM;MAXPPM]
  AUX1: 0 if < 0.9*MAXPPM else 1
  AUX2: 0 if < 0,9* MAXPPMAUX2 else 1
CMPS12
  ROLL, PITCH: range [-90;+90]
  YAW: range [0;+359]
PID computed for Roll and Pitch based on RC Command vs CMPS12 measures
  error = command – measure => error > 0 means increase command.
  PID = (0.6*error) + (0.1*sum_error*sampleTime) + (0.3*delta_error/ sampleTime)
  NB:
    The Integral component is capped to 5
    Low pass filter cut frequency at 20 Hz for the Derivative component, cuts out the high frequency noise that can drive the controller crasy
    Initial Yaw (YawInit) is subtracted from Yaw and Yaw is converted from [0;+359] to range [-180;+180]
Call MotorESC_RunMotors
  ESC_command[THROTTLE] = RC_command Throttle
  ESC_command[ROLL] = PID Roll
  ESC_command[PITCH] = PID Pitch
  ESC_command[YAW] = PID Yaw

## Slide 8: Drone processing (2/3)
MotorESC_RunMotors
  if ESC_command[THROTTLE] = 0 => Motors = MINPWM
  else:
  throttle = map(ESC_command[THROTTLE], MINPPM, MAXPPM, MINPWM, MAXPWM);
  throttle = constrain(throttle, MINPWM, MAXPWMTHRO); // to give room for PID ajustement
  PIDMIX(X,Y,Z) ESC_command[ROLL]*X + ESC_command[PITCH]*Y + ESC_command[YAW]*Z
  motor[0] = PIDMIX(+1,-1,-1); //Front Left
  motor[1] = PIDMIX(-1,-1,+1); //Front Right
  motor[2] = PIDMIX(-1,+1,-1); //Rear Right
  motor[3] = PIDMIX(+1,+1,+1); //Rear Left
  for(i=0; i< NBMOTORS; i++) {
  _motor[i] = map(_motor[i], -90, 90, -(MAXPWM-MINPWM)/2, (MAXPWM-MINPWM)/2);
  _motor[i] = _motor[i] + throttle;
  }

## Slide 9: Drone processing (3/3)
MotorESC_RunMotors (continued)
  For all motors compute:
    maxMotor = max (motor[i]- MAXPWM )
    minMotor = max (MINPWM - _motor[i])
  If maxMotor >0, then Subtract maxMotor from all motors
  If minMotor >0, then Add minMotor to all motors
  If maxMotor >0 or minMotor >0 , then Cap all motors between MINPWM and MAXPWM

## Slide 10: RC
+90 Yaw
-90 Yaw
+90 Roll
+ Front Right
+ Rear Right
-90 Roll
+Front Left
+ Rear Left
0 Throttle
+1920 Throttle
-90 Pitch
+Rear Right
+ Rear Left
+90 Pitch
+ Front Left
+ Front Right
Aux1 (0/1)
Aux2 (0/1)

## Slide 11: ESC (Electronic Speed Controler)
Configuration | Position stick during configuration | Nb beep
Brake off | Low | 1
Timing | Medium | 2
Cut | Medium | 2
Plane mode | Low | 1
Throttle response | Low | 1

## Slide 12: Special pins Arduino MEGA2560
Pin Change Interrupt 2 ISR(PCINT2_vect)
For pins PCINT16-PCINT23 (PK0- PK7), PORT K
Use pin A8 to A13 (PCINT16 to PCINT21 )
PCMSK2 – Pin Change Mask Register 2 Bit 2 – PCIF2: clear any outstanding interrupts 2
PCIFR – Pin Change Interrupt Flag Register => Bit 2 – PCIF2: clear any outstanding interrupts 2
PCICR – Pin Change Interrupt Control Register => Bit 2 – PCIE2: enable pin change interrupts 2
SPI
Pin #10: CS
pin #11->pin #51
pin #12->pin #50
pin #13->pin #52