## Slide 1
Arduino MEGA2560
Serial 1
18
TX
SD card
50
51
52
Digi
Tal
Int 1
3
Int1
I2C
20
SDA
21
SCL
IMU
CMPS12
SPI
Serial 3
15
RX
14
TX
Buzzer DFR0032
IOTWIFIClient
ESP8266
SPI
TXD
RXD
MISO
MOSI
11
SCLK
12
13
10
CS
0V
+5V
0V
Camera
LSY201
25
+5V
0V
Contact Left
26
Contact Right
27
PWM
Tilt&Pan Horiz
44
Tilt&Pan Vert.
45
Servo IR
46
Serial 2
17
RX
16
TX
IOTBlueServer
nRF52832
°C & %H DHT22
38
220 Ω
220 Ω
220 Ω
A4
A5
RTC
DS1307
SCL
SDA
Address
0x68
Address
0x60
Int 0
2
Int0
Motion
SEN0018
36
DTR / RST
39
37
35
22
23
24
19
RX

## Slide 2
HBridge
HBridge
Arduino MEGA2560
D
IGITAL
PWM
5
4
Motor right #1 In
30
+0v
31
33
32
6
7
Motor right #1 Enable
Motor right #2 Enable
Motor right #2 In
Motor right #2
(rear)
Motor right #1
(front)
Motor left #1 In
Motor left #1 Enable
Motor left #2 Enable
Motor left #2 In
Motor left #2
(rear)
Motor left #1 (front)
+7.4v
+0v
Lipo
+
+
+
+
-
-
-
-

## Slide 3: Devices (1/2)
Device | Purpose | Interface | 
RC-THROTTLE | RC Command | PPM- Interrupt PCINT16/PK0 pin A8 | 
RC-ROLL | RC Command | PPM- Interrupt PCINT17/PK1 pin A9 | 
RC-PITCH | RC Command | PPM- Interrupt PCINT18/PK2 pin A10 | 
RC-YAW | RC Command | PPM- Interrupt PCINT19/PK3 pin A11 | 
RC-AUX1 | RC Command | PPM- Interrupt PCINT20/PK4 pin A12 | 
RC-AUX2 | RC Command | PPM- Interrupt PCINT21/PK5 pin A13 | 
Motor Front Left | ESC Motor | PWM pin 3 | 
Motor Front Right | ESC Motor | PWM pin 4 | 
Motor Rear Right | ESC Motor | PWM pin 5 | 
Motor Rear Left | ESC Motor | PWM pin 6 | 

## Slide 4: Devices (2/2)
Device | Purpose | Interface | 
IMU CMPS12 | Control | I2C 0X60 | 
SD Card | Logging | SPI | 
RTC DS1307 | Logging | I2C 0x68 | 

## Slide 5: Motors
# | Position | Pin | Pin #
0 | Front Left | Motor1Pin | 3
1 | Front Right | Motor2Pin | 4
2 | Rear Right | Motor3Pin | 5
3 | Rear Left | Motor4Pin | 6

## Slide 6: Motors rotation (1/2)
0
1
3
2
Front Left
Rear Left
Front Right
Rear Right
+ Roll -
-
Pitch
+
-
Yaw
+

## Slide 7: Drone Command (1/3)
RC Command
for ROLL, PITCH, YAW: range [-90;+90]
for THROTTLE: 0 or value included in [MINPPM;MAXPPM]
for AUX1, AUX2: 0/1
CMPS12
for ROLL, PITCH: range [-90;+90]
PID computed for Roll and Pitch based on RC Command vs CMPS12
error = command – measure => error > 0 means increase command.
PID = (0.6*error) + (0.1*sum_error*sample_in_sec) + (0.3*delta_error/ sample_in_sec)
Call MotorESC_RunMotors
ESC_command[THROTTLE] = RC_command Throttle
ESC_command[ROLL] = PID Roll
ESC_command[PITCH] = PID Pitch
ESC_command[YAW] = 0

## Slide 8: Drone Command (2/3)
MotorESC_RunMotors
if ESC_command[THROTTLE] = 0 => Motors = MINPWM
else:
throttle = map(ESC_command[THROTTLE], MINPPM, MAXPPM, MINPWM, MAXPWM);
throttle = constrain(throttle, MINPWM, MAXPWMTHRO); // to give room for PID ajustement
PIDMIX(X,Y,Z) ESC_command[ROLL]*X + ESC_command[PITCH]*Y + ESC_command[YAW]*Z + ESC_command[THROTTLE]
motor[0] = PIDMIX(+1,-1,-1); //Front Left
motor[1] = PIDMIX(-1,-1,+1); //Front Right
motor[2] = PIDMIX(-1,+1,-1); //Rear Right
motor[3] = PIDMIX(+1,+1,+1); //Rear Left
for(i=0; i< NBMOTORS; i++) {
_motor[i] = map(_motor[i], -90, 90, -(MAXPWM-MINPWM)/2, (MAXPWM-MINPWM)/2);
_motor[i] = _motor[i] + throttle;
if((MAXPWM - _motor[i]) > maxMotor) maxMotor = MAXPWM - _motor[i];
if((MINPWM - _motor[i]) > minMotor) minMotor = MINPWM - _motor[i];
}

## Slide 9: Drone Command (3/3)
if (maxMotor > 0) {
for(i=0; i< NBMOTORS; i++) {
_motor[i] = _motor[i] - maxMotor;
if((MINPWM - _motor[i]) > minMotor) minMotor = MINPWM - _motor[i];
}
}
if (minMotor > 0) {
for(i=0; i< NBMOTORS; i++) {
_motor[i] = _motor[i] + minMotor;
}
}
if ((minMotor > 0) || (maxMotor > 0)) {
for(i=0; i< NBMOTORS; i++) {
_motor[i] = constrain(_motor[i], MINPWM, MAXPWM); // last cap if still needed after up and bottom cap
}
}

## Slide 10: Motors Rotation (2/2)
Roll: left/right side tilt.
  + tilted side right, speed 2 Right, slow 2 Left
  - left, speed 2 Left, slow 2 Right
Pitch: up/down tilt.
  + tilted skyward, speed 2 Front, slow 2 Rear
  - ground, speed 2 Rear, slow 2 Front
Yaw: rotation.
  + Clockwise, speed Front Left & Rear Right, slow Front Right & Rear Left
  - Counter clockwise, speed Front Right & Rear Left, slow Front Left & Rear Right

## Slide 11: Special pins Arduino MEGA2560
Interruptions
Pin #2 = interruption #0 Pin #3 = interruption #1 Pin #18 = interruption #5 Pin #19 = interruption #4 Pin #20 = interruption #3 Pin #21 = interruption #2
SPI
Pin #10: CS
pin #11->pin #51
pin #12->pin #50
pin #13->pin #52